## Slide 1
Pillar 1: MTTR & SQL Farm Modernization — Current State
120 database-related incidents, January to September 2026
Manulife
INTERNAL
1
120
Database-related incidents
0
P1 incidents recorded
0.22 hr
Shortest recovery — and it was a P2
Recovery time by priority — observed, not estimated
Priority | Incidents | Shortest MTTR | Longest MTTR
P1 | 0 | — | —
P2 | 8 | 0.22 hr | 7.58 hr
P3 | 18 | 0.23 hr | 9.25 hr
P4 / Other | 94 | — | —
Total | 120 |  | 
What the numbers tell us
Priority does not tell you how long you will be down.
Our longest recorded recovery, 9.25 hrs, was a P3 — 22% longer than the worst P2 at 7.58 hrs. A priority records the symptom raised at the time. It does not tell you how long the business is down.
There is no recovery time we can guarantee today.
P2 recovery ran from 0.22 to 7.58 hrs, P3 from 0.23 to 9.25 hrs. How long we are down is driven by what failed and what sat behind it, not by severity.
DOMINANT FAILURE MODES (one primary category per incident)
28
Performance / latency / timeout
22
Synchronisation / consistency
21
Connectivity / credentials
11
SQL / query / job error
4
Blocking / contention / deadlock
Performance, contention and index / partition design account for the largest share of incidents — these are design and capacity issues, not operator error.
9.25 hr
Longest recovery — and it was a P3
A recovery duration was recorded for 17 of the 120 incidents, and for none of the 94 P4s. Shortest and longest above are the observed extremes of those 17.

## Slide 2
If it happens again today — what we know, and what we cannot see
Manulife
INTERNAL
2
0.22 – 9.25 hr
Observed recovery range (P2 and P3)
30%
Incidents that self-recovered (36 of 120)
Unknown
Farm members with a tested DR path
What the incident record tells us
▪ Performance and contention drive the estate — 28 performance, latency or timeout, 22 synchronisation, 4 blocking. The same causes recur.
▪ Severity did not predict duration — a P3 ran longer than P2. Triage reflects the initial symptom, not the business exposure.
▪ Recovery is largely manual — batch rerun 24, restore or rollback 5, restart or failover 3. Recovery depends on people being available.
▪ 36 incidents self-recovered — the failure path worked. That is not evidence the design is sound.
What we cannot see is a P1 — an actual VM failure, a full SQL instance loss or a database loss.
It has not happened, so it has never been measured. Planning on P2 and P3 alone leaves it out P1 and it has to be factored in.
Not factored in
P1 — VM, SQL instance or database failure
What we should also discover
01
Which SQL farm members are on out-of-support versions, and which are compliant?
Sets the supportability floor and the audit exposure
02
Which have no HA design, and which DR paths have been tested regularly?
Tells us what survives a P1 event, and what does not
03
Which SQL instances and databases take longest to recover, and why?
Turns MTTR from an average into a named target list
04
Which applications can be retired, and which have no upgrade path?
Separates what we invest in from what we let retire

## Slide 3
What we are solving — Stabilize, Modernize, Scale
Manulife
INTERNAL
3
01 STABILISE Now to end 2026
▪ Make recovery measurable .
▪ Root cause analysis on the recurring performance and contention incidents
▪ Fix what recurs: query tuning, blocking, index and partition redesign
▪ Standardize runbooks so recovery is not person-dependent
Outcome: recovery becomes predictable and measurable
02 MODERNISE Early 2026 to 2027
▪ These systems were sized for what they carried when they were built — more components, more applications and far more data sit on them now
▪ Use cloud where it delivers , retain dedicated infrastructure where required, and size to current workloads .
▪ Supported SQL versions, using cloud infrastructure and current tooling where they fit for Scalable Options
Outcome: performance and stability issues resolved — systems operational and reliable
03 SCALE 2026 to 2027
▪ Scale up the members the business depends on, with HA design (Always On / FCI) where criticality justifies it
▪ A DR path that is documented, owned and actually tested
▪ Room to explore Cloud technologies to achieve same operational abilities but a headroom to scale them easily for any needs.
Outcome: capacity matched to the business, with HA and DR where criticality demands it
Modernization Focused on Operational Resilience.
We are not re-architecting what is already stable. We invest only in supportability, performance, capacity and, where criticality justifies it, HA and DR — using cloud infrastructure, current tooling and AI-assisted analysis wherever they shorten the path or let us reach a decision faster.
INVESTMENT DISCIPLINE
RETIRE
CAS and components that will be decom
NO INVESTMENT
Measure and REDESIGN
Must keep running OA / GA
WHERE WE INVEST
SUSTAIN
Both Operational and reliable
NO INVESTMENT
WHAT WE ARE DOING NOW — DISCOVER AND BASELINE
1. Draw the baseline — what we run, and how it recovers and the times .
2. Classify every SQL Instance — retire, redesign or sustain